## Slide 1
Introduction to Accelerators (Applied E&M and Relativity)
Todd Satogata / Center for Advanced Studies of Accelerators and Old Dominion
June 9 2016 GSPDA Seminar

## Slide 2: GSPDA Summer Lecture Series

## Slide 3: History: Jean-Antoine Nollet
In 1746 he gathered about two hundred monks into a circle over a 2 kilometers in circumference, with pieces of iron wire connecting them. He then discharged a battery of Leyden jars through the human chain and observed that each man reacted at substantially the same time to the electric shock, showing that the speed of electricity's propagation was very high.
Wikipedia, The Handy Physics Answer Book (Zitzewitz)

## Slide 4: The Monkotron
Nollet had
  lots of charged particles
  moving in a confined 2km ring (!)
  at very high velocities
  accelerated by high voltage
Nollet didn’t have
  controlled magnets
  controlled acceleration
  proper instrumentation
  many friends after this experiment
http://www.yproductions.com/writing/archives/twitch_token_of_such_things.html

## Slide 5: We’ve Come A Long Way Since This
1767 Lecons de Physique, Jean-Antoine Nollet
(Thomas Jefferson, coincidentally, was 24)

## Slide 6: A Beam of Particles is a Very Useful Tool
A beam of the right particles with the right energy at the right intensity can…
… or discover the secrets of the universe
Shrink a tumor | Produce cleaner energy
Spot suspicious cargo | Make a better radial tire
Clean up dirty drinking water | Map a protein
Study a nuclear explosion | Design a new drug
Make a heat-resistant cable | Diagnose a disease
Reduce nuclear waste | Detect an art forgery
Implant ions in a semiconductor | Prospect for oil
Date an archaeological find | Package a Thanksgiving turkey
Accelerators for America’s Future, DOE report, 2010

## Slide 7: A Beam of Particles is a Very Useful Tool
A beam of the right particles with the right energy at the right intensity can…
… or discover the secrets of the universe
Shrink a tumor | Produce cleaner energy
Spot suspicious cargo | Make a better radial tire
Clean up dirty drinking water | Map a protein
Study a nuclear explosion | Design a new drug
Make a heat-resistant cable | Diagnose a disease
Reduce nuclear waste | Detect an art forgery
Implant ions in a semiconductor | Prospect for oil
Date an archaeological find | Package a Thanksgiving turkey
Accelerators for America’s Future, DOE report, 2010

## Slide 8: Of Glory not a Beam is left…
A beam of the right particles with the right energy at the right intensity…
E. Dickinson (1685)

## Slide 9: Of Glory not a Beam is left…
A beam of the right particles with the right energy at the right intensity…
  Directed
  Focused
  Controlled
E. Dickinson (1685)

## Slide 10: Of Glory not a Beam is left…
A beam of the right particles with the right energy at the right intensity…
  Directed
  Focused
  Controlled
E. Dickinson (1685)

## Slide 11: The Right Particles
A beam of the right particles with the right energy at the right intensity…
  Accelerator beams are electromagnetically charged subatomic particles
  So we use electromagnetic fields to control them
Protons
Electrons
Ions
And even muons and pions and photons and neutrinos and and and…
(except neutrinos, which are always left-handed)

## Slide 12: The Right Particles
A beam of the right particles with the right energy at the right intensity…
  Accelerator beams are electromagnetically charged subatomic particles
  So we use electromagnetic fields to control them
  Lorentz Force:
Protons
Electrons
Ions
And even muons and pions and photons and neutrinos and and and…
(except neutrinos, which are always left-handed)

## Slide 13: The Right Energy
A beam of the right particles with the right energy at the right intensity…
The Loch Ness Monster, Busch Gardens Williamsburg (15 miles north of JLab)
Potential
Kinetic

## Slide 14: The Right Energy
A beam of the right particles with the right energy at the right intensity…
  Lorentz Force:

## Slide 15: The Right Energy
A beam of the right particles with the right energy at the right intensity…
  Lorentz Force:
  Electric Field:
    Force in the same direction as electric field
    We use electric fields to speed up/slow down particles

## Slide 16: The Right Energy
A beam of the right particles with the right energy at the right intensity…
  Lorentz Force:
  Electric Field:
    Force in the same direction as electric field
    We use electric fields to speed up/slow down particles
  Magnetic Field:
    Force is perpendicular to velocity and magnetic field
    We use magnetic fields to steer and focus particles

## Slide 17: The Right Energy
A beam of the right particles with the right energy at the right intensity…
  Lorentz Force:
  Electric Field:
    Force in the same direction as electric field
    We use electric fields to speed up/slow down particles
  Magnetic Field:
    Force is perpendicular to velocity and magnetic field
    We use magnetic fields to steer and focus particles
    Also a band…

## Slide 18: How Accelerators Accelerate
Electric Fields:
Created by distributions of electric charge

## Slide 19: How Accelerators Accelerate
Electric Fields:
Created by distributions of electric charge
We could use static DC charge…

## Slide 20: DC Accelerating Gaps: Cockcroft-Walton
Accelerates ions through successive electrostatic voltages
  First to get protons to >MeV
  Continuous HV applied through intermediate electrodes
  Rectifier-multipliers (voltage dividers)
  Limited by HV sparking/breakdown
  FNAL still uses a 750 kV C-W
Also example of early ion source
  H gas ionized with HV current
  Provides high current DC beam
~1930 1.4 MeV
Cavendish Lab
Source
Target
Rectifiers
Notes: First artificial nuclear reaction (1932) Li7+p -> He4 + He4

## Slide 21: DC Accelerating Gaps: Van de Graaff
How to increase voltage?
  R.J. Van de Graaff: charge transport
  Electrode (1) sprays HV charge onto insulated belt
  Carried up to spherical Faraday cage
  Removed by second electrode and distributed over sphere
Limited by discharge breakdown
  ~2MV in air
  Up to 20+ MV in SF6!
  Ancestors of Pelletrons (chains)/Laddertrons (stripes)
Notes: SF6 also happens to be the worst greenhouse gas known.
Also extremely dense. For amusement, http://www.youtube.com/watch?v=d-XbjFn3aqE

## Slide 22: Van de Graaff Popularity

## Slide 23: Van de Graaff Popularity

## Slide 24: DC Accelerating Gaps: Tandem Van de Graaff
This only works for negative ions
However, stripping need not be symmetric
  Second stage accelerates more efficiently
BNL: two Tandems (1970, 14 MV, 24m)
  Au-1 to Au+10/Au+11/Au+12 to Au+32 for RHIC
  About a total of 0.85 MeV/nucleon total energy
Reverse ion charge state in middle of Van de Graaff allows over twice the energy gain
  Source is at ground

## Slide 25: From Electrostatic to RF Acceleration
Cockcroft-Waltons and Van de Graaffs have DC voltages, E fields
What about putting on AC voltage?
  Attach consecutive electrodes to opposite polarities of ACV generator
  Electric fields between successive electrodes vary sinusoidally
  Consecutive electrodes are 180 degrees out of phase (π mode)
At the right drive frequency, particles are accelerated in each gap
  While polarity change occurs, particles are shielded in drift tubes
  To stay in phase with the RF, drift tube length or RF frequency must increase at higher energies
Pagani and Mueller 2002
Wideroe linac

## Slide 26: “Radio Frequency” RF Cavity Examples
Linear Collider
RHIC (BNL in New York)
CEBAF
1497 MHz
197 MHz
Tens of Millions of V/m!

## Slide 27: Advanced Acceleration Methods
How far do accelerating gradients go?
  Superconducting RF acceleration: ~40 MV/m
  CLIC (CERN): ~100 MV/m
    Two-beam accelerator: drive beam couples to main beam
  Dielectric wall acceleration: ~100 MV/m
    Induction accelerator, very high gradient insulators
  Dielectric wakefield acceleration: ~GV/m
  Laser plasma acceleration: ~40 GV/m
    electrons to 1 GeV in 3.3 cm
    particles ride in wake of plasma charge separation wave

## Slide 28: BELLA (Berkeley Lab) Makes the News
4.2 GeV electrons
in 9 cm
40 fs (=12 μm), 0.3 PW peak power drive laser
Multi-GeV Electron Beams from Capillary-Discharge-Guided Subpetawatt Laser Pulses in the Self- Trapping Regime
W. P. Leemans, et al., PRL 113, 245002 2014 (December 8, 2014)

## Slide 29: Applied Special Relativity
Particle accelerators are the best examples
that we have of applied special relativity
  Subatomic particles traveling very close to light speed
  Particle kinetic energies >> rest mass energies
    Electron rest mc2 equal to energy gained in 0.5 million V
    So electrons going though these accelerators are very quickly very relativistic

## Slide 30: Applied Special Relativity
Particle accelerators are the best examples
that we have of applied special relativity
  Subatomic particles traveling very close to light speed
  Particle kinetic energies >> rest mass energies
Relativistic parameters
  γ=1 (classical mechanics) to ~2.05x105 (to date) (where??)
  v=0.99999999997 c

## Slide 31: Applied Special Relativity
Particle accelerators are the best examples
that we have of applied special relativity
  Subatomic particles traveling very close to light speed
  Particle kinetic energies >> rest mass energies
Relativistic parameters
  γ=1 (classical mechanics) to ~2.05x105 (to date) (where??)
  v=0.99999999997 c
Total energy U, momentum p, and kinetic energy W

## Slide 32: Relative Relativity

## Slide 33: Relative Relativity

## Slide 34: Relative Relativity

## Slide 35: Relative Relativity

## Slide 36: “Convenient” Units
How much is a TeV?
  Energy to raise 1g about 16 um against gravity
  Energy to power 100W light bulb 1.6 ns
But many accelerators have 1010-12 particles
  Single bunch “instantaneous power” of tens of Terawatts
Highest energy observed cosmic ray
  ~300 EeV (3x1020 eV or 3x108 TeV!)

## Slide 37: “Convenient” Units
OMG particle
How much is a TeV?
  Energy to raise 1g about 16 um against gravity
  Energy to power 100W light bulb 1.6 ns
But many accelerators have 1010-12 particles
  Single bunch “instantaneous power” of tens of Terawatts
Highest energy observed cosmic ray
  ~300 EeV (3x1020 eV or 3x108 TeV!)

## Slide 38: “Convenient” Units
OMG particle
How much is a TeV?
  Energy to raise 1g about 16 um against gravity
  Energy to power 100W light bulb 1.6 ns
But many accelerators have 1010-12 particles
  Single bunch “instantaneous power” of tens of Terawatts
Highest energy observed cosmic ray
  ~300 EeV (3x1020 eV or 3x108 TeV!)

## Slide 39: “Convenient” Units
OMG particle
How much is a TeV?
  Energy to raise 1g about 16 um against gravity
  Energy to power 100W light bulb 1.6 ns
But many accelerators have 1010-12 particles
  Single bunch “instantaneous power” of tens of Terawatts
Highest energy observed cosmic ray
  ~300 EeV (3x1020 eV or 3x108 TeV!)
(125 g hamster at 100 km/hr)

## Slide 40: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Make all the particles go where we want them to go
    How do we steer and guide the particles?
  Keep the beam from getting to big or divergent
    How do we keep the particles focused together?

## Slide 41: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Make all the particles go where we want them to go
    How do we steer and guide the particles?
  Keep the beam from getting to big or divergent
    How do we keep the particles focused together?
  Lorentz Force:
    Magnetic fields dominate as v approaches c

## Slide 42: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Make all the particles go where we want them to go
    How do we steer and guide the particles?

## Slide 43: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Make all the particles go where we want them to go
    How do we steer and guide the particles?
  Use areas of constant to bend the particle paths
  Particles move in semi-circles in areas of constant
    They move in lines (circles of infinite radius) when B=0
Constant B field out of page
Zero B field
Zero B field

## Slide 44: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Make all the particles go where we want them to go
    How do we steer and guide the particles?
  Use areas of constant to bend the particle paths
  Different momentum particles bend slightly differently
    Just like a prism in classical optics
Constant B field out of page
Zero B field
Zero B field

## Slide 45: Dipole Field
The type of accelerator magnet that creates a constant magnetic field region is a dipole magnet
North
South

## Slide 46: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Keep the beam from getting to big or divergent
    How do we keep the particles focused together?

## Slide 47: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Keep the beam from getting to big or divergent
    How do we keep the particles focused together?
  Bend all particles towards design path = focusing
  B field varies linearly with displacement: B=0 at center
Zero B field
Zero B field
Linearly varying B field – zero along central path

## Slide 48: The Right Intensity
A beam of the right particles with the right energy at the right intensity…
  Keep the beam from getting to big or divergent
    How do we keep the particles focused together?
  Just like a lens in classical optics
Zero B field
Zero B field
Linearly varying B field – zero along central path

## Slide 49: Quadrupole Field
The type of accelerator magnet that creates a magnetic field region that varies linearly with position is a quadrupole magnet
North
South
South
North

## Slide 50: Accelerator Magnet Examples
Air-temperature
steel magnets
(Danfysik)
Superconducting
NbTi magnets (LHC)
0.1 to 15 Tesla! (Earth’s field 3-7x10-5 Tesla)

## Slide 51: Normal vs Superconducting Magnets
  Note high field strengths (red) where flux lines are densely packed together
LHC dipole magnets (SC)
LEP quadrupole magnet (NC)

## Slide 52: Picturing Drift and Quadrupole Motion
KL=0.5 m-1, f=2m
KL=0.1 m-1, f=20m
KL=20 m-1, f=0.05m
KL=-0.1 m-1, f=-20m
Quadrupoles act just like lenses in classical optics

## Slide 53: Putting It All Together
Horizontal particle
Position and angle
Vertical particle
Position and angle
Horizontal and
Vertical position

## Slide 54: Stretch Break

## Slide 55: A Beam of Particles is a Very Useful Tool
A beam of the right particles with the right energy at the right intensity can…
… or discover the secrets of the universe
Shrink a tumor | Produce cleaner energy
Spot suspicious cargo | Make a better radial tire
Clean up dirty drinking water | Map a protein
Study a nuclear explosion | Design a new drug
Make a heat-resistant cable | Diagnose a disease
Reduce nuclear waste | Detect an art forgery
Implant ions in a semiconductor | Prospect for oil
Date an archaeological find | Package a Thanksgiving turkey
Accelerators for America’s Future, DOE report, 2010

## Slide 56: A Beam of Particles is a Very Useful Tool
A beam of the right particles with the right energy at the right intensity can…
… or discover the secrets of the universe
Shrink a tumor | Produce cleaner energy
Spot suspicious cargo | Make a better radial tire
Clean up dirty drinking water | Map a protein
Study a nuclear explosion | Design a new drug
Make a heat-resistant cable | Diagnose a disease
Reduce nuclear waste | Detect an art forgery
Implant ions in a semiconductor | Prospect for oil
Date an archaeological find | Package a Thanksgiving turkey
Accelerators for America’s Future, DOE report, 2010

## Slide 57: Shrink a Tumor: X-Ray Radiotherapy
From the perspective of medicine
  Irradiate the cancer and spare healthy tissue
  We can use beams of radiation and particles as surgical scalpels to selectively kill cancer cells
Image courtesy of Varian/Eclipse
X-ray intensity-modulated radation therapy (IMRT)
  Commonly performed “gamma knife”
  Requires multiple directions
Can (mostly) avoid critical structures
  But still residual radiation dose
  Residual dose is high on skin, in early entry areas
  Some unpleasant side effects

## Slide 58: Shrink a Tumor: Proton Radiotherapy
http://iopscience.iop.org/0031-9155/55/12/018

## Slide 59: Shrink a Tumor: Radiotherapy Cyclotron
Distinct dose localization advantage for hadrons over X-rays
There is also present work on proton and carbon radiotherapy fast-cycling synchrotrons
Cynthia Keppel, July 14 GSPDA Lecture

## Slide 60: Produce Cleaner Energy
S. Henderson, Thorium Energy Alliance Conf 2012

## Slide 61: Produce Cleaner Energy: Thorium Reactor
S. Henderson, Thorium Energy Alliance Conf 2012

## Slide 62: Date an Archaeological Find
A 4-6 MeV accelerator in the basement of the Louvre
  Date and determine atomic constituents of antiquities
  Induces low-level nuclear emissions of charged particles
    No damage to art objects in process of analysis
  Very trace elements can be detected
    E.g. Far-East provenance
    of Ishtar statue found in
    Mesopotamia near 0 CE
Ruby-eyed ~0 CE Ishtar

## Slide 63: Map a Protein
Resolution of imaging is directly related to wavelength
  Small wavelengths can resolve molecular, atomic detail
  Smaller wavelengths can resolve electron motion
  Wavelengths: VUV into X-ray region (NSLS)
  Pulse lengths: picoseconds (10-12 s) to attoseconds (10-18 s)
  Ultra-short wavelengths/pulses: very high power (~GW)
Objectives of accelerator-based light sources
  Investigate imaging of atoms, molecules, and materials
  ... in timescales of electron motion around orbitals (~100 as!)
molecule
molecule

## Slide 64: Map a Protein
Coulomb Explosion of Lysozyme (50 fs)
Atomic and molecular dynamics occur at the fsec-scale
J. Hajdu, Uppsala

## Slide 65: Map a Protein… with Free Electron Lasers (FELs)
Free electrons can be lased
  Not a gas/liquid/solid state laser
  Capture laser in optical cavity
  Laser beam and undulator stimulate further laser emission
Very high brightness
  102-105 over older accelerators
Tunable laser frequencies
  >5-10, microwaves to X-rays
RF Electron Gun
Linac
Undulator
Optical Cavity
Laser Light
Bill Gabella, Vanderbilt

## Slide 66: Map a Protein… with LCLS-II FEL at SLAC
LCLS-II Design Report
Being built with Jefferson Lab Superconducting RF technology

## Slide 67: Discover the Secrets of the Universe
CEBAF
LHC (Switzerland)
KEKB (Japan)
RHIC (New York)

## Slide 68: Did Somebody Say CEBAF?
6-12 GeV (~1 MW) polarized electrons
1497 MHz beams
Circumference ~1300m (0.8 miles)
CW recirculating linacs
RF and magnets
RF and magnets
magnets

## Slide 69: The CEBAF Tunnel
Arc magnets
Linac RF cryomodules
Superconducting RF operates at 2K
High vacuum systems
Instrumentation/diagnostic systems
High-power electrical systems
Control system: 10k+ control points

## Slide 70: Why CEBAF?
Let’s say we want to do a diffraction/scattering experiment to get images of atomic nuclei (protons and neutrons)
  Proton charge radius: ~0.88 x 10-15 m (0.88 fm)
We also want to measure electroweak interactions
  So our probe better be EM charged and polarizable (to see asymmetric scattering from weak force parity violation)
High-energy electrons fit the bill perfectly
  Higher energies can also excite new nuclear/parton states
  Polarized beam asymmetries are sensitive to weak interaction currents

## Slide 71: How CEBAF?
A multi-GeV continuous electron beam is not common!
  Equivalent to accelerating through GV of potential
  Far far too large to create with electrostatics
Regular (non-superconducting) RF cavities?
  CW state of the art was ~2 MV/m: 2 GeV = 1 km of cavities
  We want high frequency (100s of MHz): high Ohmic losses
  This implies many 10s of MW of wall plug power!
Superconducting RF cavities!
  Requires construction of large 2K (or 4K) cryogenic facility
  But can achieve high energy, “high current” CW beams
  Original gradients: ~5 MV/m => Ee ~ 4 GeV
  The first major superconducting RF facility in the world

## Slide 72: CEBAF Reminder
RF and magnets
RF and magnets
magnets

## Slide 73: Refurbished CEBAF RF Cavities
Made out of very pure large-grain Nb
  Superconducting RF technology research is a very active area
    Includes many active control loops for consistent fields
  Nb RF technology theoretical limit: 55 MV/m
  Insulating cryomodule layers removed here for visibility

## Slide 74: CEBAF: From 6 GeV to 12 GeV

## Slide 75: C100 RF
New RF cryomodules: 4x gradient of old modules
  Adding 5 new modules doubles energy of accelerator
  Each module: 20 MV/m, ~100 MeV energy gain/module
Ilkyoung
Shin
Shahid Ahmed

## Slide 76: Thank you!!!