## Slide 1: Introduction to Accelerator Physics Spring 2018 RF Cavities
Todd Satogata (Jefferson Lab and ODU) / satogata@jlab.org
http://www.toddsatogata.net/2018-ODU-AP
Subashini De Silva (ODU) / sdesilva@jlab.org
Happy Birthday to Ovid, Mr. Rogers, and Spike Lee!
Happy Spring Equinox, National Ravioli Day, National Proposal Day,
and Extraterrestrial Abductions Day!

## Slide 2: RF Cavities
1500 MHz 5-cell
RF cavities made of different materials, in different shapes and sizes
1300 MHz 9-cell
Quarter Wave Cavity
Half Wave Cavity
Triple Spoke Cavity
Single Spoke Cavity
CESR Type Cavity (Cornell)

## Slide 3: RF Concepts and Design
Much of RF is really a review of graduate-level E&M
  See, e.g., J.D. Jackson, “Classical Electrodynamics”
  The beginning of this lecture is hopefully review
    But it’s still important so we’ll go through it
  Particularly important are cylindrical waveguides and cylindrical RF cavities
    Will find transverse boundary conditions are typically roots of Bessel functions
    TM (transverse magnetic) and TE (transverse electric) modes
    RF concepts (energy gain, gradient, stored energy, resistive losses, quality factor)

## Slide 5: 9.1: Maxwell’s Equations
Electric charge density
Electric current density

## Slide 6: Constitutive Relations and Ohm’s Law

## Slide 7: Boundary Conditions
Boundary conditions on fields at the surface between two media depend on the surface charge and current densities:
  and are continuous
  changes by the surface charge density (scalar)
  changes by the surface current density
C&M Chapter 9: no dielectric or magnetic materials

## Slide 8: Wave Equations and Symmetry
Taking the curl of each curl equation and using the identity
then gives us two identical wave equations
These linear wave equations reflect the deep symmetry between electric and magnetic fields. Harmonic solutions:

## Slide 9: Plane Wave Properties
The source-free divergence Maxwell equations imply
so the fields are both transverse to the direction
(This will be the direction in a lot of what’s to come)
Faraday’s law also implies that both fields are spatially transverse to each other

## Slide 10: Standing Waves
Note that Maxwell’s equations are linear, so any linear combination of magnetic/electric fields is also a solution.
Thus a standing wave solution is also acceptable, where there are two plane waves moving in opposite directions:

## Slide 11: 9.2: Cylindrical Waveguides
Consider a cylindrical waveguide, radius a, in z direction
  can be imaginary for attenuation down the guide
  We’ll find constraints on this cutoff wave number
  Maxwell in cylindrical coordinates (math happens) gives

## Slide 12: Transverse Electromagnetic (TEM) Modes
Various subsets of solutions are interesting
  For example, the nontrivial solutions require
  The wave number of the guide matches that of free space
  Wave propagation is similar to that of free space
  This is a TEM (transverse electromagnetic) mode
    Requires multiple separate conductors for separate potentials or free space
    Sometimes similar to polarization pictures we had before
Coaxial
cable

## Slide 13: Transverse Magnetic (TM) Modes
Maxwell’s equations are linear so superposition applies
  We can break all fields down to TE and TM modes
  TM: Transverse magnetic (Hz=0, Ez≠0)
  TE: Transverse electric (Ez=0, Hz≠0)
  TM provides particle energy gain or loss in z direction!
  Maxwell’s equations in cylindrical coordinates give
Bessel equation
SHO equation
=> n integer, real

## Slide 14: TM Mode Solutions
The radial equation has solutions of Bessel functions of first Jn(kcr) and second Nn(kcr) kind
  Toss Nn since they diverge at r=0
  Boundary conditions at r=a require Jn(kca)=0
  This gives a constraint on kc
  This mode of this field is commonly known as the TMnj mode
  The first index corresponds to theta periodicity, while the second corresponds to number of radial Bessel nodes
  TM01 is the usual fundamental accelerating mode

## Slide 15: TM Mode Visualizations
Java app visualizations are also linked to the class website
  For example, http://www.falstad.com/emwave2 (TM visualization)
    Scroll down to Circular Modes 1 or 2 in first pulldown

## Slide 16: Cavity Modes
Dave McGinnis, FNAL

## Slide 17: Cutoff Frequency
It’s easy to see that there is a minimum frequency for our waveguide that obeys the boundary conditions
  Modes at lower frequencies will suffer resistance
  Dispersion relation in terms of radial boundary condition zero
  A propagating wave must have real group velocity
  This gives the expected lower bound on the frequency
  Wavelength of lowest cutoff frequency for j=1 is

## Slide 18: Cylindrical RF Cavities
What happens if we close two ends of a waveguide?
  With the correct length corresponding to the longitudinal wavelength, we can produce longitudinal standing waves
  Can produce long-standing waves over a full linac
  Modes have another index for longitudinal periodicity
Simplified “tuna fish can”
RF cavity model
TM010 mode

## Slide 19: Boundary Conditions
Additional boundary conditions at end-cap conductors at z=0 and z=l

## Slide 20: TEnjm Modes
Longitudinal
periodicity

## Slide 21: TEnjm ModesModes in a Cylindrical Cavity
Xnj is the jth root of Jn
X’nj is the jth root of J’n

## Slide 22: TMnjm Modes
Longitudinal
periodicity
TM010 is (again) the preferred acceleration mode

## Slide 23: TMnjm Modes in a Cylindrical Cavity
Xnj is the jth root of Jn
X’nj is the jth root of J’n

## Slide 24: Bessel Functions and Roots

## Slide 25: Problem (1): Calculate Frequencies
Radius (a) |  | 
Length (l) |  | 
Freq. of TM010 |  | 
Freq. of TM020 |  | 
Freq. of TM110 |  | 
Freq. of TE011 |  | 
Freq. of TE111 |  | 

## Slide 26: TM010 Mode
E
TM010 mode
Magnetic Field
Electric Field
Cut off frequency:

## Slide 27: TM020 Mode
Peggs/Satogata

## Slide 28: TM110 Mode
Peggs/Satogata

## Slide 29: Equivalent Circuit
A TM010 cavity looks much like a lumped LRC circuit
  Ends are capacitive
  Stored magnetic energy is inductive
  Currents move over resistive walls
E, H fields 90 degrees out of phase
  Electric field is concentrated near axis
  Magnetic field is concentrated at outer cylindrical wall

## Slide 30: Accelerating Energy Gain
Lorentz force
Energy gain
Gradient
L
E
H
2a
No contribution
At r=0

## Slide 31: Elliptical Accelerating Cavities

## Slide 32: Stored Energy for TM010 in a Cylindrical Cavity
C&M 9.82
Stored energy

## Slide 33: Surface Resistance and Power Losses
There is still non-zero power loss for finite resistivity
  Surface resistance: resistance to current flow per unit area
  This isn’t just applicable to RF cavities, but to transmission lines, power lines, waveguides, etc – anywhere that electromagnetic fields are interacting with a resistive media

## Slide 34: TM010 Average Power Loss
ends
sides
Compare to stored energy
  Both vary like square of field, square of Bessel root
  Dimensional area vs dimensional volume in stored energy

## Slide 35: Conductivity and Skin Depth
For high conductivity, , charges move freely enough to keep electric field lines perpendicular to surface (RF oscillations are adiabatic vs movement of charges)
  Copper:
  Conductivity condition holds for very high frequencies (1015 Hz)
For this condition
  Inside the conductor, the fields drop off exponentially
e.g. for Copper

## Slide 36: Anomalous Skin Effect
Conductivity really depends on the frequency and mean time between electron interactions (or inverse temperature)
  Classical limit is , adiabatic field wrt electron interactions
  For non-classical limit, no longer applies since electrons see changing fields between single interactions
Normal skin effect
Anomalous skin effect
Asymptotic value
Skin depth
Mean free path
Reuter and Sondheimer, Proc. Roy. Soc. A195 (1948), from Calatroni SRF’11 Electrodynamics Tutorial

## Slide 37: Quality Factor
Ratio of average stored energy to average power lost (or energy dissipated) during one RF cycle
  How many cycles does it take to dissipate its energy?
  High Q: nondissipative resonator
  Copper RF: Q~103 to 106
  SRF: Q up to 1011

## Slide 38: Niobium Cavity SRF “Q Slope” Problem